Kria KV260 setup
What you’ll need:
- KV260 Power supply and Adapter (12V, 3A)
- MicroSD Card 16GB or Above
- USB-A to micro-B Cable
- Raspberry Pi Camera
- Ethernet Cable

PetaLinux installation
- Download the Kria KV260 image from the Xilinx webpage to your PC.
- Download the Balena Etcher image flashing tool
- Follow the instructions within Balena Ethcher to flash the image to the SD card

Hardware setup
- Insert the microSD card containing the boot image in the microSD card slot (J11)
- Connect the micro-B end of the USB-A to micro B cable to J4
- Connect the Raspberry Pi Camera Module to J9
- Connect to a monitor/display with the the HDMI cable
- Connect the DC power supply to J12

Booting the board
- Using a terminal emulator of your choice such as Putty, open a terminal with a baud rate of 115200.
- Power up the KV260 board and observe the power LEDs illuminate and the Linux boot response appear on the UART.
- Once the board has booted to the Linux command prompt, enable the root user with the command ‘sudo su -l root’.
- Verify internet connectivity with the command ‘ping 8.8.8.8’

Building and installing VVAS
- Clone the following repository containing the VVAS file structure onto the host PC with the following command: ‘git clone --recurse-submodules https://github.com/Xilinx/VVAS.git’
- Build VVAS with the following command within the repository folder: ‘./build_install_vvas.sh Edge’
- Copy VVAS to the KV260 board using either a USB stick or the following network transfer command:
  ‘scp install/vvas_installer.tar.gz <board ip>:/’
- On the KV260 board, run the following commands to install VVAS:
  ‘cd /’
  ‘tar -xvf vvas_installer.tar.gz’
- VVAS should now be installed and ready to run on the KV260 board.